## Slide 1: Vending Machine Controller
Team J
Younsuk Choi, Yuming (Leano) Wang, Muhammad Emaan Sajid
2025.06.24
Hardware Engineering Lab
Summer Term 2025
Page 1

## Slide 2: Concepts with diagrams_block diagram
Hardware Engineering Lab
Summer Term 2025
Page 2
Selection of items using switches
Display the names and the prices of the items using 8 digits of seven segment display
Insertion coins using push buttons
Display the inserted coin amounts using 8 digits of seven segment display
Display the current state using LEDs

## Slide 3: Concepts with diagrams_state machine diagram
Hardware Engineering Lab
Summer Term 2025
Page 3

## Slide 4: VHDL Code Implementations VendingMachine_Top.vhd
Hardware Engineering Lab
Summer Term 2025
Page 4

## Slide 5: VHDL Code Implementations FSM_Controller.vhd Part 1
Hardware Engineering Lab
Summer Term 2025
Page 5
string_to_ascii
converts 8-characters string to a 64-bit std_logic_vector
format_price_to_string
converts 14-bit unsigned integer(cents) to 4-digit ASCII character string

## Slide 6: VHDL Code Implementations FSM_Controller.vhd Part 2_processes
Hardware Engineering Lab
Summer Term 2025
Page 6
Moore’s FSM

## Slide 7: VHDL Code Implementations FSM_Controller.vhd Part 3_Process
Hardware Engineering Lab
Summer Term 2025
Page 7

## Slide 8: VHDL Code Implementations Coin_Handler.vhd
Hardware Engineering Lab
Summer Term 2025
Page 8

## Slide 9: VHDL Code Implementations Display_Manager.vhd
Hardware Engineering Lab
Summer Term 2025
Page 9

## Slide 10: Verification with Test Benches_Results:FSM_Controller
Test Cases:
Test case 1: Check if the state transitions from IDLE to DISPLAY when the BTNC is pressed
Test case 2: Check if the state transitions from DISPLAY to INSERT when no switch is selected
Test case 3: Check if the state transitions from DISPLAY to INSERT when switch 1 is selected
Test case 4: Check if the state transitions from INSERT to DISPENSE when inserted amount is lower than the price of the item
Test case 5: Check if the state transitions from INSERT to DISPENSE when inserted amount is greater or equal to the price of the item
Test case 6: Check if the state transitions from DISPENSE to IDLE when a switch is still on
Test case 7: Check if the state transitions from DISPENSE to IDLE when a switch is finally off.
Test case 8: Check if the state transitions from IDLE to DISPLAY when the BTNC is pressed.
Test case 9: Check if the item 1 is displayed correctly if the SW(0) is on. (SW_tb = “001”)
Test case 10: Check if the item 2 is displayed correctly if the SW(1) is on. (SW_tb = “010”)
Test case 11: Check if the item 3 is displayed correctly if the SW(2) is on. (SW_tb = “100”)
Test case 12: Check if the inserted amount (50) is correctly being displayed on the right 4 digits of 7 segment display.
Test case 13: Check if the inserted amount (150) allows state transition to DISPENSE and the correct change is displayed on the 7 segment display.
Test case 14: Check if the state transitions from DISPENSE to IDLE when a switch is still on.
Test case 15: Check if the state transitions from DISPENSE to IDLE when the switch is finally off.
Hardware Engineering Lab
Summer Term 2025
Page 10
One hot coding

## Slide 11: Test Benches_Results:FSM_Controller
Hardware Engineering Lab
Summer Term 2025
Page 10

## Slide 12: Verification with Test Benches_Results:Coin_Handler
Test Cases:
‘01234567’
‘89 AEObc’
‘ghlor ’
‘colA0130’
‘bEEr0150’
‘h2o 0090’
Hardware Engineering Lab
Summer Term 2025
Page 12

## Slide 13: Test Benches_Results:Coin_Handler
Hardware Engineering Lab
Summer Term 2025
Page 11

## Slide 14: Verification with Test Benches_Results:Display_Manager
Test Cases:
Insert 10 cents and see if the inserted amount is 10 cents
Insert 20 cents and see if the inserted amount is 30 cents
Insert 50 cents and see if the inserted amount is 80 cents
Insert 100 cents = 1 euro and see if the inserted amount is 180 cents
Reset the test
Hardware Engineering Lab
Summer Term 2025
Page 14

## Slide 15: Test Benches_Results:Display_Manager
Hardware Engineering Lab
Summer Term 2025
Page 12

## Slide 16: FPGA Implementations_constraint file
Hardware Engineering Lab
Summer Term 2025
Page 16

## Slide 17: FPGA Simulations
Videos
Simulation in Real Time
Hardware Engineering Lab
Summer Term 2025
Page 17

## Slide 18: PCB Prototyping
PCB design is a process of designing printed circuit boards in which we electrically connect electronic components. Some known process of PCB Design
Find requirement according the target group or client
Select the design tools
Schematics drawing
Components placements
Routing
Design Rules Check
Gerber file generation
Simulation and testing
Prototyping
Final production
Hardware Engineering Lab
Summer Term 2025
Page 18

## Slide 19: PCB Prototyping
After discussion and deep analysis we select these elements for our PCB
Two 7 segment display
power supply
Resistors and Capacitors
Central component is the Nexus A7 XC7A100T FPGA, handling all control logic and I/O
Connected to multiple push buttons for item selection and user interaction.
PNP and NPN transistors control outputs like relays or motors, acting as switches via FPGA signals.
Schematics
3D View
Page 19
Schematics
Hardware Engineering Lab
Summer Term 2025

## Slide 20: PCB Prototyping
Our custom PCB Board Design Process
I did follow some steps to creating our custom PCB
Initially I did install Kicad 9.0 for designing
I did create a folder for save our custom board.
I start add components from library to schematics
After complete schematics then I start routing
I added external plugin for auto routing like freerouting
I added some connection manually
I am able to see the nice 3D view of custom PCB
Now I am able to generate Gerber file
Page 20
Hardware Engineering Lab
Summer Term 2025
Fig: PCB Layout

## Slide 21: BOM Cost and Gerber files
BOM stands for Bill of Material that:
Is a detailed list of all components used in the PCB.
Includes part numbers, quantities, footprints, and specifications.
Helps manufacturers know what parts to purchase and assemble.
Generated automatically by the PCB design software (e.g., KiCad).
Gerber files are:
set of files that describe physical layout of PCB.
Includes copper layers, silkscreen, solder mask, and drill holes.
Used by PCB manufacturers to fabricate the board.
Page 21
Hardware Engineering Lab
Summer Term 2025

## Slide 22
Thank you for listening
We are ready to show simulation on FPGA and answer your questions
Hardware Engineering Lab
Summer Term 2025
Page 1